## Slide 1: Tank Battle
B05901016 王珽
B05901064 林承德
B05901185 戴慕潔

## Slide 2: Outline
Game Rules
Game Structure
  Display
  Joystick
  Game State
  Tank & Shell
  RandomMap
Demo

## Slide 3: Game Rules
1

## Slide 4: START
Place your screenshot here
Press left together to start

## Slide 5: Joystick
↑
←
→
↓
fire
Moving direction

## Slide 6
time
How many lives do you have
Player 2
Player 1
The wall can be hit through if you hit more than 3 times
Random map
(8 maps in total)

## Slide 7: END
Place your screenshot here
Press left together to start the next game

## Slide 8: Game Structures
2

## Slide 9: DISPLAY
VGA : 640 x 480 resolution with frequency 60Hz
We divided the screen to 64 x 48 grids
  Top 4 rows : Status bar
  Tank : 5 x 5 grids
  Shell : 1 x 1 grid
  Wall : 1 x 1 grid

## Slide 10: DISPLAY
K-means Clustering
  k-means clustering aims to partition n observations into k clusters
  We use k = 8 or 16 in this case
  Reduce bits per pixel from 24 to 3 or 4.
  Pros : centers are dependent on picture.

## Slide 11: DISPLAY
Origin Image
Resize to 320x240
K-means with k=16
Change color
(implement on FPGA)

## Slide 12: DISPLAY
Remove watermark
Coloring
Crop
Resize 50x50
K-means, k=8
Tank0_label.dat
Tank0_center.dat
Tank1_label.txt
Tank1_center.dat

## Slide 13: Joystick
Arduino Joystick Shield
  5 buttons on it. o_debounce : up, down, left, right o_neg : fire
  Connected 7 lines to GPIO on FPGA (5 buttons + VDD + GND)
  Change the threshold in Debounce

## Slide 14: Game States
START
END
GAME
Press left together
Press left together
One of the tanks dies
Implement the collision cases:
Shell hits the wall
Tank hits the wall
Shell hits the other tank
Tank hits the other tank

## Slide 15: Tank & Shell
Position
  X-position
  Y-position
Speed
  Tank: Change position once every four frames
  Shell: Change position once every 400000 cycles
Health (Tank only)
  Initial value of 3

## Slide 16: RandomMap
Provide map information to Gamestate
Random Number Generator
  Use lab1’s code
  RNG changes number eyery clock, but we only change map when someone dies.
Life
  Initial value of 3
  When the wall dies, it will send 0 to Gamestae.

## Slide 17: Demo
3

## Slide 18: Thanks!